## Slide 1: 8051 addressing modes

## Slide 2: six types of addressing modes
Immediate Addressing Mode
Register Addressing Mode
Register Specific Addressing mode
Direct Addressing Mode
Indirect Addressing Mode
Indexed Addressing Mode

## Slide 3: Immediate addressing mode
In this Immediate Addressing Mode, the data is provided in the instruction itself. The data is provided immediately after the opcode. These are some examples of Immediate Addressing Mode.
MOV A, #0AFH;
MOV R3, #45H;
MOV DPTR, #FE00H;
In these instructions, the # symbol is used for immediate data

## Slide 4: Register addressing mode
In the register addressing mode the source or destination data should be present in a register (R0 to R7). These are some examples of Register Addressing Mode.
MOV A, R5;
MOV R2, #45H;
MOV R0, A;

## Slide 5: Register Specific Addressing mode
In the Register specific (implied) addressing mode, there will be a single operand. These types of instruction can work on specific registers only. These types of instructions are also known as register specific instruction.
RLA;
SWAP A;

## Slide 6: Direct Addressing Mode
In the Direct Addressing Mode, the source or destination address is specified by using 8-bit data in the instruction. Only the internal data memory can be used in this mode. Here some of the examples of direct Addressing Mode.
MOV 80H, R6;
MOV R2, 45H;
MOV R0, 05H;

## Slide 7: Indirect Addressing Mode
In indirect addressing the instruction specifies a register which contains the address of the operand. Both internal and external RAM can be indirectly addressed.
The address register for 8-bit addresses can be R0 or R1 of the selected register bank. The address register for 16-bit addresses can only be the 16-bit “data pointer” register, DPTR.
MOVX A, @R0
MOVX @DPTR,A

## Slide 8: Indexed Addressing Mode
In the indexed addressing mode, the source memory can only be accessed from program memory only. The destination operand is always the register A.
Only Program Memory can be addressed with indexed addressing, and it can only be read. This addressing mode is intended for reading look-up tables in Program Memory.
MOVC A, @A+PC;
MOVC A, @A+DPTR;